## Slide 1
Department of Electronics Engineering
Walchand College of Engineering, Sangli
(Government-Aided Autonomous Institute)
Project A.Y. 2025-2026
Smart Interactive Vision with Object Tracking and Voice Command
Under the guidance of
Prof. Sachin Ruikar
Group No: 13

## Slide 2
TEAM MEMBERS (GROUP - 13)
  Gayatri Dabhade
  Achala Paradeshi
  Akshat Gupta
  PRN - 22410052
  PRN - 22410053
  PRN - 22410063

## Slide 3
OVERVIEW
  Introduction
  Literature Survey
  Project Idea
  Components
  Block Diagram
  Working
  Objectives
  Application
  Future Scope

## Slide 4
  INTRODUCTION
This project presents a real-time intelligent vision system capable of face detection, tracking, and voice-based interaction using computer vision and embedded systems. The system uses OpenCV and MediaPipe for accurate face detection through a USB camera and calculates face coordinates in real time. A proportional controller with EMA smoothing is applied to achieve stable and smooth servo movement. The processed commands are sent through USB serial communication to an Arduino Uno, which controls SG90 servo motors for camera pan and tilt motion. Compared to the earlier Raspberry Pi and Wi-Fi-based design, the current architecture uses direct USB communication, reducing latency and simplifying deployment. The project demonstrates an efficient, low-cost, and responsive face-tracking platform using a standard laptop and Arduino microcontroller.

## Slide 5
  LITERATURE SURVEY
  Viola-Jones Face Detection (2001)
    Introduced Haar Cascade face detection
    Enabled real-time face tracking
    Limited performance in poor lighting and side poses
  YOLO Object Detection (2016)
    Real-time deep learning object detection
    High speed and accuracy
    Inspired lightweight detection systems like MediaPipe
  Servo-Controlled Tracking (2020)
    Combined computer vision with servo motors
    Used microcontroller-based face tracking
    Introduced error-based servo angle correction using P-controller

## Slide 6
  LITERATURE SURVEY
  MediaPipe Framework (2019)
    Lightweight and fast face detection framework
    Works efficiently on CPU without GPU
    Used in this project for low-latency face tracking
  ArcFace / InsightFace (2019)
    Advanced face recognition using deep learning
    Generates accurate facial embeddings
    Supports real-time identity recognition
  DeepFace Emotion Analysis
    Detects facial emotions using CNN models
    Identifies emotions like happy, sad, angry, neutral
    Useful for smart interactive systems

## Slide 7
  PROBLEM STATEMENT
Limitations of Traditional Systems
  Inconsistent Tracking
Mechanical play and open-loop control cause imprecise face centering.
  High Latency
HTTP/Wi-Fi based protocols introduce 100–200 ms delays.
  Poor Lighting Robustness
Traditional detectors fail under dynamic lighting or fast motion.
  Complex Hardware Setup
Raspberry Pi requires full Linux OS, SSH configuration, and GPIO library management.
  High Component Cost
Using an SBC solely for servo PWM generation increases system cost (₹4,000–5,000).

## Slide 8
  PROPOSED SOLUTION
This project proposes an intelligent, vision-guided tracking system implemented on a laptop that offloads servo actuation to an Arduino Uno microcontroller via USB serial. The key design decision is the separation of concerns:
• The laptop runs all computationally intensive tasks: face detection (MediaPipe), face recognition (ArcFace), emotion analysis (DeepFace), Pcontroller logic, and the Flask web server.
• The Arduino Uno handles only servo PWM generation—a task perfectly matched to a low-cost 8-bit microcontroller—receiving pre-computed pan and tilt angles over a reliable wired serial link.

## Slide 9
Develop a real-time face detection & recognition system using OpenCV, MediaPipe, and InsightFace via a USB webcam.
  OBJECTIVES
1.
Implement a closed-loop P-controller with EMA smoothing for jitter-free servo tracking.
2.
Integrate Arduino Uno as a dedicated servo controller over USB serial (pyserial at 115,200 baud).
3.
Design a two-axis pan–tilt mechanism using two SG90 servos (Pan 40°–140°, Tilt 55°–125°).
4.
Build a Flask web application with MJPEG streaming, SQLite attendance DB, and REST API.
5.

## Slide 10
Build a Flask web application with MJPEG streaming, SQLite attendance DB, and REST API.
  OBJECTIVES
5.
Integrate Google TTS + pygame for non-blocking voice feedback on recognition events.
6.
Ensure reliability under variable lighting, multiple simultaneous faces, and rapid head movements.
7.
Create a modular, scalable architecture extensible for surveillance, attendance & assistive tech.
8.

## Slide 11
HARDWARE COMPONENTS
640×480 @ 30 fps
USB 2.0 plug-and-play
Mounted on tilt servo bracket
  USB Webcam
USB / 3.5 mm input
speech_recognition library
Commands: start, stop, identify
  Microphone
ATmega328P 16 MHz
32 KB Flash, Hardware PWM
UART 115,200 bps
  Arduino Uno R3
Compact active speaker
gTTS + pygame.mixer
Priority-queued TTS playback
  Speaker
180° micro servo
1.8 kg·cm @ 4.8 V
50 Hz PWM, 500–2400 μs
  SG90 Servo (×2)
4×AA or USB power bank
≈1.2 A capacity
Powers both servos independently
  External 5 V PSU

## Slide 12
SOFTWARE STACK
•OpenCV — frame capture & processing
•MediaPipe BlazeFace — face bounding box detection
•InsightFace (ArcFace) — 512-d face embeddings
•DeepFace — emotion classification (happy/sad/angry…)
  Vision
•arduino_serial.py — ArduinoBridge class (pyserial)
•servo_ctrl.py — P-controller + EMA smoothing
•25 px deadzone to suppress servo chatter
•Servo.h on Arduino — hardware PWM at 50 Hz
  Control
•Flask (app.py) — web server & REST API
•MJPEG /video_feed streaming endpoint
•SQLAlchemy + SQLite — Person & Attendance ORM
•JavaScript (fetch) — live dashboard updates
  Web & DB
640×480 @ 30 fps
•gTTS — text-to-speech MP3 synthesis
•pygame.mixer — non-blocking audio playback
•speech_recognition — Google STT voice cmds
•Priority queue — urgent alerts interrupt TTS
Mounted on tilt servo bracket
  Voice

## Slide 13
  HARDWARE ASSEMBLY

## Slide 14
  BLOCK DIAGRAM

## Slide 15
  FLOW CHART

## Slide 16
  WORKING
FaceTrack operates as a continuous closed-loop pipeline running at 30 fps across three parallel threads:
  Thread 1 captures frames from the USB webcam, flips them, draws annotations, and streams MJPEG to the browser dashboard.
  Thread 2 runs InsightFace detection at ~12 fps, assigns stable track IDs using IoU matching, and updates the servo target centroid.
  Thread 3 compares ArcFace 512-d embeddings against the SQLite database via cosine similarity, logs attendance, and classifies emotion using DeepFace.
The P-controller computes error = face_cx − 320, applies EMA smoothing, and sends new_angle += Kp × error as a "pan, tilt" serial command to the Arduino Uno at 115,200 baud. The Arduino calls Servo.write() on PWM pins 9 and 10, physically recentring the camera. As the face reaches the frame centre, error → 0 and the servo holds still — completing the feedback loop.
Unknown faces trigger an instant TTS alert and web badge. Recognised persons are auto-logged to SQLite with timestamp, emotion, and confidence score.

## Slide 17
  RESULTS
Peak recognition performance: Akshat 79%, Gayatri 83% — both under frontal lighting. Session duration 1093 s (≈18 min) logged without identity dropout. Servo tracking dot visible at face centre confirming active P-controller operation.
  Dual Known Subjects (Best Accuracy)
Akshat (72%, yellow) identified among two unregistered subjects — Unknown #1 (red) and Unknown (orange, primary). UNKNOWN cards show 0 visits and no timestamps, confirming zero false-positive assignments. Dashboard accessed remotely from 10.187.95.217:5001.
  Group with Unknown Alert

## Slide 18
  RESULTS
Most demanding test: 4 simultaneous faces. Akshat (66%) labelled PRIMARY; Unknown #1, #2, #3 assigned red boxes. Emotion HAPPY detected. Attendance auto-logged: Main Entrance · 60 s. Zero false identities.
  Crowd Scene (4 Faces)
Three simultaneous detections: Akshat B Gupta (61%, yellow), Unknown #2 (red), Gayatri (70%, yellow). Emotion SAD labelled. Per-person stat panel shows confidence bar, visit count, and snapshot thumbnails.
  Mixed Recognition (3 faces)

## Slide 19
  RESULTS
Camera Feed page: Achala recognised at 80% (yellow), two unknowns (orange, red), emotion FEAR displayed. Camera Info panel confirms 640×480, MediaPipe FD, ≥80% threshold, status RUNNING. Alert log shows auto camera reconnection events.
  Live Camera Feed Dashboard

## Slide 20
  APPLICATIONS
  Smart Attendance System
Automatically logs check-in/check-out with emotion data via face recognition, eliminating manual registers.
  Assistive Technology
Helps differently-abled users interact through gaze tracking and voice commands without physical touch.
  Robotics Research Platform
Low-cost, modular testbed for pan-tilt tracking, servo control, and vision-based navigation experiments.
  Interactive Kiosks
Enables hands-free, voice-controlled interaction at reception desks or public information terminals.
  Security Surveillance
Detects and tracks unknown individuals in real time, triggering alerts and saving snapshots for review.

## Slide 21
  Successfully demonstrated real-time face detection, recognition, and servo tracking on a standard laptop + Arduino Uno.
  Replacing Raspberry Pi with direct USB serial achieved lower latency, improved stability, reduced complexity, and lower cost.
  Proportional controller with EMA smoothing and deadzone filtering ensures stable tracking even under noisy detection.
  Flask dashboard delivers live video streaming, attendance management, enrollment, and AI-powered monitoring.
  Modular architecture is readily extensible for smart surveillance, automated attendance, and assistive robotics.
CONCLUSION

## Slide 22
  Replace SG90 with stepper motor for smoother full 360° rotation; add multi-camera coverage.
  Integrate YOLOv8 for improved multi-object tracking; deploy on NVIDIA Jetson Nano / Raspberry Pi 5.
  Add gesture-based control (MediaPipe Hands) and voice commands via OpenAI Whisper.
  Cloud integration via Firebase / AWS; vibration stabilisation using IMU sensors.
  Reinforcement learning-based adaptive controller to auto-optimise tracking without manual calibration.
  FUTURE SCOPE

## Slide 23
  Viola P. & Jones M. (2001). Rapid Object Detection using a Boosted Cascade of Simple Features. IEEE CVPR.
  Redmon J. et al. (2016). You Only Look Once: Unified, Real-Time Object Detection. IEEE CVPR.
  Lugaresi C. et al. (2019). MediaPipe: A Framework for Building Perception Pipelines. IEEE CVPR Workshops.
  Deng J. et al. (2019). ArcFace: Additive Angular Margin Loss for Deep Face Recognition. IEEE CVPR.
  Taigman Y. et al. (2014). DeepFace: Closing the Gap to Human-Level Performance in Face Verification. IEEE CVPR.
  OpenCV Documentation — https://opencv.org
  Shinde A. & Kulkarni P. (2024). Smart Mirror Interface Using Interactive Vision Systems. IEEE HCI Conference.
  MediaPipe Documentation — https://mediapipe.dev
  Arduino Servo Motor Control Basics — https://www.arduino.cc
REFERENCES

## Slide 24
  THANK YOU